## Slide 1: MBEYA UNIVERSITY OF SCIENCE AND TECHNOLOGY
AUTOMOTIVE TECHNOLOGY III
ME 6203
Mr. Mbawala, SB
Mechanical And Industrial Engineering Department

## Slide 2: ASSESSMENT METHODS
The course will be assessed by continuous assessment (CA) and End of semester examination 1. Continuous Assessment (50%)
Practical 25%
Theory 25%
Test 1-10%
Individual Assign-5%
Group Assgn-10%
2. Semester Examination (50%)

## Slide 3: Lecture 1; Clutch

## Slide 4: What to be Learned
Define Clutch
Classification of clutches
Identify components of clutch
Describe how clutch works
Describe maintenance procedure of different types of clutches
Perform maintenance of different types of clutches

## Slide 5: Introduction
A clutch is a machine member used to connect a driving shaft to a driven shaft so that the driven shaft may be started or stopped at will, without stopping the driving shaft
Clutch is used in manual transmission system in a vehicle, or the working parts of any machine. e.g. fan clutch
The engagement and disengagement of the shafts is obtained by means of a clutch

## Slide 6: Types of Clutch
There are two main types of clutches commonly used in engineering practice :
a. Positive clutches
b. Friction clutches

## Slide 7: Types of Clutch
Positive Clutches
The positive clutches are used when a positive drive is required (no slip).
The simplest type of a positive clutch is a jaw or claw clutch.
The jaw clutch permits one shaft to drive another through a direct contact of interlocking jaws or teeth

## Slide 8: Types of Clutch
Positive Clutches cont..
Jaw clutch consists of two halves; one of them permanently fastened to the driver shaft.
The other half is movable and is attached to the driven shaft.
It can freely slide axially on the shaft, but cannot turn due to feather key.
They can transmit power in both directions; they are used when it is not necessary to engage or disengage under load.

## Slide 10: Types of Clutch
Advantages of positive clutch
They do not slip
They can transmit large torque
Develop no heat during engagement and disengagement because of rigid interlocking (no friction).

## Slide 11: Types of Clutch
Disadvantages of positive clutch
Engagement of clutch cannot be possible at high speed
While starting some relative motion may be required to engage.

## Slide 12: Types of Clutch
b. Friction Clutches A friction clutch has its principal application in the transmission of power of shafts and machines which must be started and stopped frequently.
Its application is also found in cases in which power is to be delivered to machines partially or fully loaded.

## Slide 13: Types of Friction Clutches
Though there are many types of friction clutches, yet the following are important from the subject point of view : 1. Disc or plate clutches (single disc or multiple disc clutch), 2. Cone clutches, and 3. Centrifugal clutches We will concentrate on disc(plate) clutch

## Slide 14: Disc clutches (single disc or multiple disc)
The clutch assembly is located between the engine and the transmission or transaxle. The purpose and function of a clutch include the following:
To connect and transmit engine torque to the transmission/transaxle
To disconnect the engine from the transmission/transaxle to permit the engine to remain running when the vehicle is stopped and to permit the transmission/transaxle to be shifted
To dampen and absorb engine impulses and drive train vibrations
To provide a smooth engagement and disengagement between the engine and the transmission/transaxle

## Slide 15: Components of Clutch System
The main components of clutch System
Flywheel
Clutch plate
Pressure plate
Release mechanism

## Slide 19
1. Flywheel
The engine flywheel serves four basic purposes:
Smoothens out or dampens engine power pulses
Provides the connection point for the starter motor to crank the engine
Provides the application surface for the clutch friction disc
Absorbs some of the heat created by clutch operation

## Slide 21
2. Clutch plate
The clutch disc/plate is round with a splined center hole that slips over the splines of the input shaft of the transmission/ transaxle.
Clutch plate transmit power from flywheel to input shaft of gearbox through friction materials which riveted to both sides of the clutch disc (one side touches the flywheel of the engine and the other side touches the friction surface of the pressure plate).
Friction materials operate in high heat and pressure.

## Slide 22
For many years, asbestos was the most common material used in both clutch and brake linings.
However, it is no longer used because inhaling tiny particles of asbestos causes lung damage.
Today, clutch friction material may contain paper, cotton, and bits of copper or brass wire with resin holding the mixture together.
CAUTION: Always take precautions when working around clutch lining material and assume that it contains asbestos.
2. Clutch plate cont..

## Slide 24
3. Pressure plate
The purpose of the pressure plate is to exert a force on the clutch disc so that engine torque can be transmitted from the engine to the transmission/transaxle.
Pressure plate is bolted to the back of the flywheel, and the clutch disc is sandwiched in between the flywheel and the pressure plate.
The assembly consists of the pressure plate cover, face, springs, and sometimes release levers
Since the pressure plate assembly is bolted to the flywheel, it rotates at all times. But the clutch disc only rotates when the clutch is engaged.

## Slide 25
3. Pressure plate cont..
Pressure Plate Cover
The cover houses the components of the pressure plate assembly and holds them together. It provides the means to bolt the assembly to the flywheel.
Pressure Plate Face
Like the flywheel, the pressure plate face is usually made of iron, and the friction surface is precision machined. The pressure plate springs are seated or attached to the back of the face. The pressure plate face moves back and forth inside the cover as the clutch pedal is operated.
Pressure Plate Springs
There are two main types of pressure plate spring systems:
a. Coil spring
b. Diaphragm spring.

## Slide 26
a. Coil spring style
This style of pressure plate uses coil springs and three or four release arms. A coil-spring-style pressure plate is also called the lever style because it uses levers to compress the coil spring
Operation of a coil spring pressure plate is similar to a diaphragm spring pressure plate, but it has a few additional parts.
Instead of one large spring, this type has a number of smaller coil springs placed around the back of the pressure plate face.
The release bearing does not act directly on the springs, but rather on release levers that pivot and push or pull the pressure plate face away from the clutch disc and flywheel.
Coil spring pressure plates are better suited than the diaphragm type for heavier-duty applications.

## Slide 27
b. Diaphragm spring style
Diaphragm spring is a round, dish-shaped spring with numerous segments radiating towards the center.
The spring action is similar to that of an old-style. A release bearing, actuated by the clutch pedal, acts directly on the inner ends of the spring, overcoming the spring tension that engages the clutch, this action disengages the clutch. Diaphragm springs require less force from the release bearing to disengage the clutch, they use less space, and the assembly is lighter and more easily balanced than the other main type of pressure plate (coil spring)
The driver must push harder on the clutch pedal to disengage a coil spring clutch than to disengage a comparable diaphragm spring design.

## Slide 28
The diaphragm clutch has replaced the coil spring type because the diaphragm type has the following advantages: ● It is not affected by high speeds (coil springs can be thrown outwards) ● The low pedal force makes for easy operation ● It is light and compact i.e. few components and less space ● The clamping force increases or at least remains constant as the friction lining on the plate wears

## Slide 30
4. Release mechanism
It involves
i. Clutch pedal
ii. Mechanical linkage/Cable/Hydraulic circuit
iii. Release fork
iv. Release bearing

## Slide 31
i. Clutch pedal
The clutch pedal is located on the floor to the left of the brake pedal. When pressed, clutch disengages which eliminates the transmission of power from the engine to the transmission and when released, clutch engages and transmit power from the engine to the transmission.
Return springs are used to help bring the release mechanism and clutch pedal home to their normal positions when the clutch is engaged.
4. Release mechanism

## Slide 33
ii. Mechanical linkage/Cable/Hydraulic circuit
These are the ways in which clutch pedal movement is transmitted to the clutch release fork
Mechanical Linkage
This method uses a system of levers and rods to disengage the clutch.
Many different arrangements have been used. Mechanical linkage is mainly found on some older vehicles.
4. Release mechanism

## Slide 34
Cable
A steel cable attached to the clutch pedal moves back and forth inside a flexible housing as the clutch pedal is operated.
The housing is mounted in a stationary position.
It usually has a threaded sleeve on one end to allow the lengthening and shortening of the cable for clutch adjustment.
Some cable release systems are self-adjusting, using a ratcheting mechanism on the clutch pedal to take up slack as the clutch disc wears.
The cable release system is inexpensive and simple in design and operation, but it is more prone to wear and binding than other types. It is always used in motor cycle

## Slide 36
Hydraulic Circuit
The hydraulic clutch release system uses a clutch cylinder (also called a clutch master cylinder), a hydraulic line, and a slave cylinder(release cylinder) to transfer clutch pedal motion to the clutch fork.
The hydraulic system is very much like a brake hydraulic system, and clutch systems commonly use brake fluid as well
A fluid reservoir may be built into the unit, or there may be a separate reservoir remotely mounted above the unit for easier access.

## Slide 37
Hydraulic Circuit cont..
The master cylinder is like a single-circuit brake master cylinder.
The hydraulic line consists of metal tubing and rubber hoses, just like a brake system.
It runs from the clutch cylinder to the slave cylinder.
The slave cylinder is mounted on the bell housing near the clutch fork.
It is much like a wheel cylinder on a drum brake with one piston and actuating pin.

## Slide 39
iii. Clutch fork
This is also part of the clutch release mechanism. Also called a release arm, release fork or throw-out lever.
Clutch fork transmits movement from the external parts of the release mechanism to the release bearing.
The fork extends through a hole in the clutch housing to reach the external parts of the release mechanism.
A protective rubber boot fits in the hole to prevent contaminants and debris from entering the clutch housing.
4. Release mechanism

## Slide 41
iv. Release bearing
The throw-out (release) bearing is attached to the clutch fork and rides on the fingers of the pressure plate.
The clutch operating system moves the clutch release bearing when the driver presses or releases the clutch pedal.
The release bearing presses against the diaphragm spring fingers or coil spring levers.
This takes spring force off the pressure plate so that it no longer clamps the friction disc against the flywheel.
4. Release mechanism

## Slide 42
iv. Release bearing cont..
When the release mechanism is properly adjusted, there is a small clearance gap between the throw-out bearing and the release levers/diaphragm spring, so the bearing only has to spin during clutch disengagement.
This reduces wear on the bearing, and results in a small amount of free travel, or free play at the clutch pedal.
The amount of free travel will be specified in the service information, usually about an inch. However, some vehicles with "self-adjusting" clutch engagement mechanisms use a special bearing that is designed to remain in contact with the pressure plate at all times
4. Release mechanism

## Slide 44
Other parts in the system
Pilot bearing
Bell housing
Clutch safety switch

## Slide 45
Pilot Bearing
The pilot bearing or bushing fits into the center of the crankshaft, usually with a light press fit.
It supports the input shaft of the transmission and keeps it from moving off center.
This is especially important when engaging the clutch.
Other parts in the system

## Slide 47
Clutch Housing
The clutch housing is also called the bell housing, and it encloses the clutch assembly.
It bolts to the back of the engine, and the manual transmission is bolted to the back of it. On some vehicles, the clutch housing is part of the transmission case.
Clutch Start Switch
Modern vehicles have a Clutch Start Switch that prevents cranking the engine with the transmission in gear unless the clutch pedal is depressed.
This is a safety feature designed to prevent the vehicle from lurching or the engine from suddenly starting if the starter motor is operated while the clutch is engaged and the transmission is in gear. The switch is part of the ignition/starter circuit.
Other parts in the system

## Slide 49: How Clutch Works
Clutch operates on the principle of friction
When two surfaces are brought in contact and are held against each other due to friction between them, they can be used to transmit power.
If one is rotated, then other also rotates.
One surface is connected to source of power and other to the one receives the power.
Thus, clutch is nothing but a combination of two friction surfaces.

## Slide 50
How Clutch Works cont..
When the driver depresses the clutch pedal, a throw-out bearing is forced against the fingers of the pressure plate.
When force is exerted on the center of the pressure plate, the pressure is released from the clutch disc that has been forced against the engine flywheel.
With the pressure removed from the clutch disc, the engine can be operated without transferring torque to the transmission/transaxle.

## Slide 51
How Clutch Works
This also permits the transmission/transaxle to be shifted because a shift cannot be made if the transmission/transaxle is transferring engine torque.
When the driver reduces force on the clutch pedal, the pedal return spring and the pressure plate spring combine to return the clutch pedal to its at-rest position.
When the clutch pedal moves up, the pressure on the throw-out bearing is released and the force against the pressure plate spring(s) is released allowing the force of the pressure plate to clamp the clutch disc tightly between the flywheel and the pressure plate allowing the torque to be transmitted from engine to gear box as before.

## Slide 53: Clutch Troubleshooting
An automotive clutch normally provides dependable service for thousands of miles. However, stop and go traffic will wear out a clutch quicker than highway driving.
Every time a clutch is engaged, the clutch disc and other components are subjected to considerable heat, friction, and wear
Driver abuse commonly causes premature clutch troubles. For instance, "riding the clutch," resting your foot on the clutch pedal while driving, and other driving errors can cause early clutch failure

## Slide 54: Clutch Troubleshooting
Perform drive test by
Checking the action of the clutch pedal
listen for unusual noises
Feel for clutch pedal vibrations
Gather as much information as you can on the operation of the clutch.
Use these information's, your knowledge of clutch principles and a service manual troubleshooting chart to determine which components are faulty

## Slide 55: Clutch Troubleshooting
The following are the clutch problems
Clutch Slipping
Clutch Grabbing
Clutch Dragging
Abnormal noises
Vibrations
It is important to know the symptoms produced by these problems and the parts that might be causing them

## Slide 56: Clutch Troubleshooting
Clutch Slipping
Slipping occurs when the driven disc fails to rotate at the same speed as the driving members when the clutch is fully engaged This condition results whenever the clutch pressure plate fails to hold the disc tight against the face of the flywheel

## Slide 57: Clutch Troubleshooting
Clutch Slipping cont..
Causes of clutch slipping
Oil or grease on the friction linings
Friction linings worn out
Scored faces on the flywheel or pressure plate
A broken engine mount
Lack of free play at the clutch pedal
Insufficient clamping force

## Slide 58: Clutch Troubleshooting
NOTE
The term clutch slipping should not, of course, be confused with slipping the clutch, since slipping the clutch is determined by driver control.
The ability of a friction clutch to slip before full engagement is a decided advantage, because it allows shock-free connection to be made between the engine and gearbox

## Slide 59: Clutch Troubleshooting
Clutch Grabbing
When alternating torques occur in the slip phase (e.g., due to friction value fluctuations) and causes vibrations of the driveline, this is called clutch grab.
Instead of slipping evenly, the clutch grips suddenly, then loses contact.
A grabbing clutch will produce a very severe vibration or jerking motion when the vehicle is accelerated from a standstill.
Even when the driver slowly releases the clutch pedal, it will seem like the clutch pedal is being pumped rapidly up and down.

## Slide 60: Clutch Troubleshooting
Clutch Grabbing cont..
Causes of Clutch Grabbing
Oil or grease on the disc facings
Loose transmission mounts and worn engine mounts
Loose disc facings
Broken parts in the clutch, such as broken disc facings, broken facing springs, or a broken pressure plate, will also cause grabbing.

## Slide 61: Clutch Troubleshooting
Clutch Dragging
This type of clutch complaint(problem) will always become evident when changing gear.
It has the effect of making gear engagement both difficult and noisy, because the center plate continues to be dragged round even though the clutch pedal is fully depressed for disengagement

## Slide 62: Clutch Troubleshooting
Clutch Dragging cont..
Causes of Clutch Dragging
Clutch linings are cracked or buckled
Clutch plate seized on the gearbox input shaft splines
Release bearing defective
Insufficiently effective pedal travel (excessive ‘free’ movement on the pedal or slave cylinder push rod)
Rusted or damaged transmission input shaft
Hydraulic system defective (due usually to then loss of most if not all of the hydraulic oil)

## Slide 63: Factors that can reduce the service life of the clutch are:
Extensive stop-and-go city driving
Frequent severe duty, such as towing or hauling
Contamination (such as oil leaking from the engine or transmission)
Driver misuse or abuse

## Slide 64: Check for
Clutch Pedal Adjustment Clutch Pedal Height
Clutch Pedal Free Play
Clutch remove and installation

## Slide 65
THANKS