## Slide 1: Lecture 2; Manual Gearbox

## Slide 2: What to be learned
Define manual gear box
Identify components of manual gear box
Describe components of manual gear box
Describe maintenance procedures for manual gear box
Perform maintenance procedures for manual gear box

## Slide 3: Introduction
A gearbox is a system that uses integrated gears with a specific arrangement to transmit the power.
There are different types of gear box with different designs and mechanisms but the aim is the same.

## Slide 4: Introduction
Functions of a Gear Box
Perform gear reduction so as to provide high torque at the time of starting vehicle acceleration, climbing up the hill
Gear box provides a reverse gear for driving the vehicle in reverse direction.
To provide more than one forward speeds by providing more than one gear ratios.
Provides neutral position for different purpose (pushing/towing, starting)
Gear box acts as a brake

## Slide 5: Introduction
The following are the types of Gear Box used in Automotive
Manual gear box
Automatic gear box
Automated manual gear box
Continuous variable Gear box

## Slide 6: Manual gear Box
A Manual gear Box is also known as manual transmission, standard transmission or stick shift transmission.
This is the type of gear box in which gear changes require the driver to select the gear by operating a gear stick and clutch

## Slide 7: Types of Manual gear box
This type of transmission is further categorized into three types
Sliding mesh gear box
Constant mesh gear box
Synchromesh gear box

## Slide 8: i. Sliding Mesh Gear Box
Gears are changed by sliding one gear on the other
It consists of three shafts; main shaft, clutch shaft(top shaft) and a counter shaft.
In a four speed gear box (which includes one reverse gear), the counter shaft has four gears which are rigidly connected to it.
Clutch shaft has one gear and main shaft has two gears.
All gears used are spur gears.

## Slide 9: i. Sliding Mesh Gear Box Cont..
The two gears on the main shaft can slide in the horizontal (co axial)direction along the splines of the main shaft. However, the gears on the counter shaft cannot slide.
The clutch gear is rigidly fixed to the clutch shaft. It is always connected to the countershaft drive gear

## Slide 12: ii. Constant mesh gear box
The constant mesh transmission has parallel shafts with gears in constant mesh.
In neutral, the gears are free running but, when shifted, they are locked to their shafts by sliding collars.
All forward gears of the countershaft are in constant mesh with the main shaft gears, which are free to rotate.

## Slide 13: ii. Constant mesh gear box Cont..
Reverse can either be a sliding collar or a constant mesh gear.
The sliding collar is splined to the main shaft, and therefore, the main shaft rotates with the sliding collar.
This principle is carried out when the shift lever moves from one speed to the next.

## Slide 16: iii. Synchromesh Transmission
The synchromesh transmission also has gears in constant mesh. However, gears can be selected without clashing or grinding by synchronizing the speeds of the mating part before they engage.
The construction of the synchromesh transmission is the same as that of the constant mesh transmission with the exception that a synchronizer has been added

## Slide 17: iii. Synchromesh Transmission Cont..
The synchronizer accelerates or slows down the rotation of the shaft and gear until both are rotating at the same speed and can be locked together without a gear clash.
Since the vehicle is normally standing still when it is shifted into reverse gear, a synchronizer is not ordinarily used on the reverse gear

## Slide 19: Transmission Construction
The manual transmission is made of the following components
Transmission Case
Extension Housing
Transmission Shafts
Transmission Gears
Synchronizers
Shift Forks
Shift Linkage and Levers

## Slide 20: Transmission Construction
a) Transmission Case
The transmission case provides support for the bearings and shafts, as well as an enclosure for lubricating oil.
A manual transmission case is cast from either iron or aluminum.
Because they are lighter in weight, aluminum cases are preferred.
A drain plug and fill plug are provided for servicing.
The drain plug is located on then bottom of the case, whereas the fill plug is located on the side

## Slide 21: Transmission Construction
b) Extension Housing
It is also known as the tail shaft housing, the extension housing bolts to the rear of the transmission case.
It encloses and holds the transmission output shaft and rear oil seal.
A gasket is used to seal the mating surfaces between the transmission case and the extension housing.

## Slide 22: Transmission case Extension housing

## Slide 23: Transmission Construction
c) Transmission Shafts
A manual transmission has four steel shafts mounted inside the transmission case. These shafts are
Input shaft
Countershaft
Main shaft
Reverse idler shaft

## Slide 24: Transmission Construction
c) Transmission Shafts cont..
a. Input shaft
The input shaft, also known as the clutch shaft or top shaft, transfers rotation from the clutch disc to the countershaft gears .
The outer end of the shaft is splined and the inner end has a machined gear that meshes with the countershaft.
A bearing in the transmission case supports the input shaft in the case.
Anytime the clutch disc turns, the input shaft gear and gears on the countershaft turn

## Slide 25: Transmission Construction
c) Transmission Shafts cont..
b. Countershaft
The countershaft, also known as the cluster gear shaft or lay shaft, holds the countershaft gear into mesh with the input shaft gear and other gears in the transmission main shaft
It is located slightly below and to one side of the clutch shaft. the gears on counter shaft rotate with it that is to say no relative motion between shaft and gears
This shaft rotates any time clutch is engaged since it is connected to top shaft

## Slide 26: Transmission Construction
c) Transmission Shafts cont..
c. Main Shaft
The main shaft, also called the output shaft, holds the output gears and synchronizers.
The rear of the shaft extends to the rear of the extension housing where it connects to the drive shaft to turn the wheel of the vehicle.
Gears on the shaft are free to rotate, but the synchronizers are locked on the shaft by splines (in case of constant mesh and synchromesh gear boxes)
The synchronizers will only turn when the shaft itself turns

## Slide 27: Transmission Construction
c) Transmission Shafts cont..
d. Reverse Idler Shaft
The reverse idler shaft is a short shaft that supports the reverse idle gear.
It mounts stationary in the transmission case about halfway between the countershaft and output shaft, allowing the reverse idle gear to mesh with both shafts.

## Slide 28: Transmission Construction
d) Transmission Gears
Transmission gears can be classified into four groups
Input gear
Countershaft gears
Main shaft gears
Reverse idler gear
The input gear turns the countershaft gears, the countershaft gears turns the main shaft gears, and, when engaged, the reverse idler gear.

## Slide 30: Transmission Construction
d) Transmission Gears cont..
In low gear, a small gear on the countershaft drives a larger gear on the main shaft, providing for a high gear ratio for accelerating.
Then, in high gear, a larger countershaft gear turns a small main shaft gear or a gear of equal size, resulting in a low gear ratio, allowing the vehicle to move faster.
When reverse is engaged, power flows from the countershaft gear, to the reverse idler gear, and to the engaged main shaft gear.
This action reverses main shaft rotation

## Slide 31: Transmission Construction
e) Synchronizers
The synchronizer is a drum or sleeve that slides back and forth on the splined main shaft by means of the shifting fork.
A transmission synchronizer has two functions: 1. Lock the main shaft gear to the main shaft 2. Prevent the gear from clashing or grinding during shifting
When the synchronizer is moved along the main shaft, the cones act as a clutch.
Upon touching the gear that is to be engaged, the main shaft is accelerated or slowed down until the speeds of the main shaft and gear are synchronized

## Slide 32: Transmission Construction
f) Shift Forks
Shift forks fit around the synchronizer sleeves to transfer movement to the sleeves from the shift linkage.
The shift fork sits in a groove cut into the synchronizer sleeve.
The linkage rod or shifting rail connects the shift fork to the operator’s shift lever.
As the lever moves, the linkage or rail moves the shift fork and synchronizer sleeve to engage the correct transmission gear.

## Slide 34: Transmission Construction
g) Shift Linkage and Levers
There are two types of shift linkages used on manual transmissions, which are external rod and the internal shift rail.
They both perform the same function.
They connect the shift lever with the shift fork mechanism.
The transmission shift lever assembly can be moved to cause movement of the shift linkage, shift forks, and synchronizers.

## Slide 35: Transmission Construction
g) Shift Linkage and Levers cont..
The shift lever may be either floor mounted or column mounted, depending upon the manufacturer.
Floor-mounted shift levers are generally used with an internal shift rail linkage, whereas column-mounted shift levers are generally used with an external rod linkage.

## Slide 39: Transmission Power Flow
Now that you understand the main parts and operation of a manual transmission, we will examine the power flow through a simple three-speed unit.
The principles are the same on transmissions with more speeds.

## Slide 43: Gear box Problems
The most gear box problems are
Hard-to-shift gears
Noise
leakage

## Slide 44: Gear box Problem’s Diagnosis
Hard-to-shift Problem
Several reasons can cause a manual transmission to be difficult to shift (engage and disengage the gears) including
Clutch not fully disengaging
Worn synchronizer
Worn, cracked, or loose shift forks
Excessive input- or main-shaft end play
Improper lubrication

## Slide 45: Gear box Problem’s Diagnosis
Gearbox Noisy
Worn bearings
Worn gears
Insufficient oil in gearbox
Incorrect grade oil

## Slide 46: Gear box Problem’s Diagnosis
leakage
Damaged oil seals
Cracks on cases
Overfilling of oil

## Slide 47: Gear Box Maintenance
Some of common checks that should be carried out on the gear box
The gear box selector linkages should be checked for signs of wear and should be lubricated
The gear box may need to be drained of oil and refilled with new, using he recommended type and grade at suitable intervals
The gear box casing should be inspected for signs of damage or oil leakage from the various oil seals
The gearbox mountings and securing bots should be checked for security and sign of deterioration