## Slide 1: Lecture 3; Automatic Gearbox

## Slide 2: This presentation will explore
Define Automatic gear box
Identify components of Automatic gear box
Describe components of Automatic gear box
Describe maintenance procedures for Automatic gear box

## Slide 3: Introduction
An automatic gear box is multi-speed transmission used in motor vehicles that does not require driver input to change gears under normal driving.
An automatic gearbox is one of the most complex systems in the vehicle.

## Slide 4: Introduction
Automatic transmissions contain mechanical systems, hydraulic systems, electrical systems and computer controls, all working together in perfect harmony.
This automatic transmission obtains different gear ratios using planetary gears

## Slide 5: Automatic Gear Box Construction
Basic Components of Automatic gear box
Torque Converter
Oil pump
Transmission case/Housing
Planetary (Epicyclic) Gearsets
Transmission Shafts
Band brake and clutch
Valve body

## Slide 7: I. Torque Converter
The torque converter is a fluid coupling that sits between the engine and the transmission.
It has two primary functions in terms of transmitting torque:
Transfers power from the engine to the transmission input shaft
Multiplies engine torque output

## Slide 8: I. Torque Converter
The torque converter couples the engine to the transmission. Its principle of operation can be demonstrated by two electric fans.
One fan power cord is connected to the AC supply and faces the other.
The air flow created by this fan causes the second fan to rotate, even though it is not connected to the supply.
A torque converter uses oil instead of air to perform the turning motion.

## Slide 10
Torque Converter Constructions
Housing - Made from two parts, an outer housing and an impeller. They are precision welded together and oil filled.
Impeller - (Driving fan) provides power to drive turbine. It contains blades that direct oil flow
Turbine - (Driven fan) contains blades that receive oil and redirect it, to produce a turning force.
Stator - Redirects oil flow from turbine to impeller, using blades
Torque Converter

## Slide 12
Torque Converter Operation
The converter housing is bolted to the flexplate of the engine
The housing and the impeller therefore turn at engine speed.
As the impeller spins, oil is flung outward. A vacuum is created in the centre of the impeller, which draws in more oil.
The turbine is connected to the input shaft of the transmission system.
It is turned by oil entering its blades. The blades force the oil toward the centre of the turbine. Oil exits the turbine in the opposite direction from impeller rotation, due to turbine design.
Torque Converter

## Slide 13
Torque Converter Operation
The stator is designed to redirect oil flow, so that it assists the impeller. It can only spin in one direction, against turbine oil flow.
At low engine speeds, the turbine turns at a lower speed than the impeller, producing a gain in output torque. This is ideal for moving a vehicle from stop, This is known as torque multiplication.
As engine speed increases, torque multiplication reduces until the speed of the turbine approaches that of the impeller (3000 RPM plus).
Torque Converter

## Slide 14
Turbine
Stator
Impeller
Flexplate
Housing
Oil flow

## Slide 15: II. Oil Pump
The hydraulic system is a complex maze of passages and tubes.
It uses pressurized transmission fluid to control transmission and torque converter operations.
The fluid also cools and lubricates components.
The Oil Pump provides a constant supply of pressurized fluid.

## Slide 16: II. Oil Pump cont..
It is directly connected to a flange on the torque converter housing and turns at engine speed.
The pump contains two gears, the inner gear, which is driven at engine speed, drives the outer gear.
Fluid is drawn up from the pan on one side of the crescent and forced into the hydraulic system on the other side.

## Slide 18: III. Transmission housing
A transmission housing encloses all the parts of the transmission
The transmission housing is typically made of aluminum.
Besides protecting all the moving gears of the transmission, the converter housing on modern cars has various sensors that track input rotational speed from the engine and output rotational speed to the rest of the car.

## Slide 19: Transmission housing cont.…
There are four main parts of the transmission housing
Converter Housing - Attaches the transmission to the engine, houses the converter and is usually made of aluminium.
Main Transmission Case -
Holds the components of the transmission system(gears, band, clutches, shafts.
Oil Pan - Holds the hydraulic oil and is sealed by a gasket.
Extension Housing - Protects and houses the output shaft and is sealed by a gasket.

## Slide 21: IV. Planetary (Epicyclic) Gearsets
In an automatic transmission, planetary gearsets are used to provide forward and reverse gear ratios.
The gears rotate, but never move in a lateral direction
The basic planetary gear set consists of a sun gear, a ring gear, planet gears and Planet carrier .

## Slide 22: IV. Planetary (Epicyclic) Gearsets Cont..
Sun Gear - Middle gear around which the other gears revolve.
Planet Gears - Usually two or more gears that mesh with, and revolve around, the sun gear.
Planet carrier-holds the planet gears together
Ring Gear - Surrounds and meshes with the planet gears.

## Slide 24: IV. Planetary (Epicyclic) Gearsets Cont..
Ring gear clamped - sun gear and planet carrier both rotate in the same direction (e.g. clockwise).
Sun gear clamped - planet carrier and ring gear both rotate in the same direction (e.g. clockwise).
Planet carrier clamped - sun gear rotates in one direction (e.g. clockwise), the ring gear rotates in the other direction (e.g. counter-clockwise).

## Slide 26: IV. Planetary (Epicyclic) Gearsets Cont..
Planetary Reduction
When the output shaft rotates slower than the input shaft, an increase in output torque is achieved. This is obtained by using gear reduction. There are two typical methods:
a. Sun gear clamped - Input is applied to the ring gear, the planet gears move around the sun gear, the planet carrier is the output.
Ring Gear - Input
Planet Carrier - Output
Sun Gear - Clamped

## Slide 27: IV. Planetary (Epicyclic) Gearsets Cont..
Planetary Reduction cont..
b. Ring gear clamped - Input is applied to the sun gear, the planet carrier is turned by the planet gears to become the output.
Ring Gear - Clamped
Planet Carrier - Output
Sun Gear - Input
In both cases, the direction of input and output rotation is the same.

## Slide 29: IV. Planetary (Epicyclic) Gearsets Cont..
Overdrive
When the output shaft rotates faster than the input shaft, an increase in vehicle speed is achieved, at the cost of reduced output torque. This is obtained by using overdrive. There are two typical methods:
a. Ring gear clamped - Input is applied to the planet carrier and the output is taken from the sun gear.
Ring Gear - Clamped
Planet Carrier - Input
Sun Gear - Output

## Slide 30: IV. Planetary (Epicyclic) Gearsets Cont..
Overdrive cont..
b. Sun gear clamped - Input is applied to the planet carrier and the ring gear is turned by the planet gears to become the output.
Ring Gear - Output
Planet Carrier - Input
Sun Gear - Clamped

## Slide 32: IV. Planetary (Epicyclic) Gearsets Cont..
Reverse
a. Planet carrier clamped - The input is applied to the sun gear and the output is taken from the ring gear.
Ring Gear - Output
Planet Carrier - Clamped
Sun Gear - Input

## Slide 33: IV. Planetary (Epicyclic) Gearsets Cont..
b. Planet carrier clamped - The input is applied to the ring gear and the output is taken from the sun gear.
Ring Gear - Input
Planet Carrier - Clamped
Sun Gear - Output
In both cases, the output will turn in the opposite direction from the input

## Slide 35: IV. Planetary (Epicyclic) Gearsets Cont..
Direct Drive
If two gears are locked together, the third gear is directly driven by the other two. This is known as direct drive.
In the diagram below, the sun gear and planet carrier are locked together.
The ring gear is forced to rotate at the same speed as the locked gears.

## Slide 37: IV. Planetary (Epicyclic) Gearsets Cont..
Rules of Planetary Gears
To determine the gear condition in a simple planetary gear set always look at what the carrier is doing.
If ever the carrier is an output in a simple planetary gear set, the condition will be a forward reduction.
If ever the carrier is held in a simple planetary gear set, the condition will be reversed.
If ever the carrier is input in a simple planetary gear set, the condition will be overdrive

## Slide 38: V. Transmission Shafts
In AT there is no direct connection between input shaft and output shaft, so there is intermediate shaft between the two- Transfers torque to the drive shaft
Input shaft
Intermediate shaft
Output shaft

## Slide 39: VI. Bands and clutches
In order for the automatic transmission to change gears, various parts of the planetary gear set must be connected to the input shaft (from the engine) while others must be held stationary.
This is done through the use of bands and clutches.
Bands are steel straps with friction material on the inside that are wrapped around a planetary gear set to hold a part of the gear train assembly from turning in order to achieve a particular gear ratio..

## Slide 40: VI. Band brake and clutch cont..
The band is tightened by the use of a hydraulic piston called a servo.
Clutch: A device used to lock two (2) components together in order to transmit motion. Primarily used for engaging the input shaft to the gear assembly.
Clutches use multiple discs which are squeezed together by a large ring-type piston.

## Slide 41: VI. Band brake and clutch cont..
The clutch casing is usually driven by the input shaft. When fluid is directed from the pump to the clutch, the fluid forces the piston forward clamping the discs together so that they all rotate as one along with the component that is connected to the clutch.
The high-pressure fluid from the pump is circulated and directed by a series of valves referred to as the valve body in order to change gears as well as lubricate the transmission.

## Slide 42
Clutch Operation
With no hydraulic pressure applied, the release springs hold the driving and driven discs disengaged and free to revolve independently of each other (A). The input shaft drives the clutch hub, but not the drum or output shaft.

## Slide 43
When hydraulic pressure is applied, the piston forces the driving discs and the driven discs together to clamp the hub to the drum so that they turn together (B) as one unit.

## Slide 45: VI. Band brake and clutch cont..
The input shaft is connected to the ring gear.
The Output shaft is connected to the planet carrier, which is also connected to a Multi-disk clutch pack.
The sun gear is connected to a drum that is also connected to the other half of the clutch pack.
Surrounding the outside of the drum is a band that can be tightened around the drum when required to prevent the drum with the attached sun gear from turning.

## Slide 47: VI. Band brake and clutch cont..
The clutch pack is used, to lock the planet carrier with the sun gear forcing both to turn at the same speed.
If both the clutch pack and the band were released, the system would be in neutral.
Turning the input shaft would turn the planet gears against the sun gear, but since nothing is holding the sun gear, it will spin free and have no effect on the output shaft.

## Slide 48: VII. Valve body
All automatic transmission systems have a valve body which serves as the “brain” of the transmission.
It's essentially a maze-like and has dozens of various passages and channels within the valve body which direct the flow of pressurized hydraulic fluid to different valves in order to activate the right clutch pack or band and shift to the most appropriate gear based on the current driving situation
The valve body contains a manual valve, which is directly connected to the gear shift handle. It covers and uncovers various passages, depending upon handle position.

## Slide 49
Types of Valve Body
There are two main types of valve body
Electronic Valve Body
Hydraulic Valve Body
VII. Valve body

## Slide 51: How an Automatic Transmission Works
After starting the engine
The engine sends power to the torque convertor’s pump(impeller)
The pump sends power to the torque converter’s turbine via transmission fluid
The turbine is connected to a central shaft that connects to the transmission.
As the turbine spins, the shaft spins, sending power to the first planetary gear set of the transmission.

## Slide 52
Depending on which multiple disc clutch or brake band is engaged in the transmission, the power from the torque converter will either cause the sun gear, the planetary carrier, or the ring gear of the planetary gear system to move or stay stationary.
Depending on which parts of the planetary gear system are moving or not determines the gear ratio. Whatever planetary gear arrangement it have, will determine the amount of power the transmission sends to the rest of the drive train.
That, broadly speaking, is how an automatic transmission works. There are sensors and valves that regulate and modify things, but that’s the basic gist of it.

## Slide 54: Common Symptoms in Automatic Transmission Problems
Harsh or delayed “garage shifts
Incorrect up or down shifting
Banging or knocking sounds
Gear slippage
Check engine light on
Smells like its burning
Low or Leaking Transmission Fluid

## Slide 57: Transmission service
Drain transmission fluid
Remove and clean the oil pan
Inspect the fluid condition, evidence of metal or clutch lining material in pan and any evidence of sludge.
Full transmission flush if needed
Remove, clean and replace the filter
Check and adjust the bands and controls