## Slide 1: Lecture 6: Braking System

## Slide 2: What to be learned
Define brake
Identify different types of the braking system
Describe different types of the braking system
Describe maintenance procedure for different types of the braking system
Perform maintenance on different types of the braking system

## Slide 3: Introduction
Braking System is a mechanism in the motor vehicle which is used to slow down or stopping the vehicle to rest by converting the kinetic energy of the moving vehicle to heat energy
Several factors can influence vehicle braking, they are
Road conditions
Weight of the vehicle
Load on the wheel during stopping
Driver maneuverability
Condition of the tires on the vehicle

## Slide 4: Introduction
Braking Performance
When we talk about the performance of brake system, we refer mainly to the vehicle’s stopping distance.
The stopping distance is the sum of distance covered during the reaction time and the metres it takes to stop the vehicle.
The traditional way to measure brake performance of a vehicle is to measure its stopping distance.

## Slide 5: Introduction
The stopping distance depends on numerous factors:
The speed of the vehicle when it starts to brake
The gradient and surface of the road
The air resistance
The efficiency of brake system
The state of the driver
Condition of the tire

## Slide 6: Introduction
Note: Heat always reduces the coefficient of friction between two objects. Hence, high temperatures may cause brakes to fail.
The loss of brake effectiveness due to heat created during prolonged hard braking is called brake fade.
If the brakes create more heat than they can dissipate, the friction coefficient reduces, which causes the brakes to fade.

## Slide 7: Types of brake system
Braking system is categorized according to different criteria as
According to Media of power transfer
Mechanical brakes
Hydraulic Brakes
Air Brakes
Air-Hydraulic Brakes
Vacuum Brakes
Electric Brakes
Electromagnetic brakes

## Slide 8: Types of brake system
According to mode of actuations on foundation brake
Disc brake
Drum brake
According to Service provided
Service brake
Emergency brake

## Slide 9: Hydraulic Brakes
Hydraulics is the use of a liquid under pressure to transfer force or motion, or to increase an applied force.
The pressure on a liquid is called Hydraulic Pressure.
And the brakes which are operated by means of hydraulic pressure are called Hydraulic Brakes.
These brakes are based on the principle of Pascal’s law.

## Slide 10: Hydraulic Brakes
Pascal’s law
States that
“The pressure exerted anywhere in a mass of confined liquid is transmitted undiminished in all directions throughout the liquid.”

## Slide 12: Hydraulic Brakes
Advantages of Hydraulic Brakes
Equal braking effort to all the four wheels
Less rate of wear (due to absence of joints compared to mechanical brakes)
Force multiplication (or divisions) very easily just by changing the size of one piston and cylinder relative to other.
Disadvantages of Hydraulic Brakes
Even slight leakage of air into the braking system makes it useless(poor performance).
The brake shoes are liable to get ruined if the brake fluid leaks out.

## Slide 13: Brake Split
Brake split is the configuration of brake pipes in hydraulic brake system.
There are three layouts of hydraulic brake system used in cars and light trucks;
Front-to-rear
Diagonal arrangement
Triangular - split brake system

## Slide 15: Brake Subsystems
Automotive brake systems can be broken down into several different sub-systems:
• Apply system
• Boost system
• Hydraulic system
• Wheel/foundation brakes
• Balance control system
• Warning system

## Slide 17: Components of Hydraulic Brakes
Pedal and linkages
Brake booster
Master cylinder
Hose and pipe
Regulating valves
Foundation brakes

## Slide 18: Components of Hydraulic Brakes
Pedal assembly
A brake pedal consists of an arm, pad and pivot attachments.
A linkage is connected to the pedal and this transmits both force and movement to the master cylinder

## Slide 19: Components of Hydraulic Brakes
Brake booster
The brake booster serves to amplify the foot pressure generated when the brake pedal is depressed.
This has the effect of reducing the manual effort required for actuation. Boosters are invariably combined with the master cylinder assembly.

## Slide 20: Components of Hydraulic Brakes
Master Cylinder
The master cylinder is the heart of hydraulic brake system.
It converts the force exerted on the brake pedal into hydraulic pressure to apply the brakes.
The fluid inside acts like a liquid linkage between the master cylinder's pistons and the wheel cylinders.
The master cylinder is able to do its job because brake fluid is incompressible, that means no bubbles or air pockets in the brake lines, master cylinder or the wheel cylinders.

## Slide 21: Components of Hydraulic Brakes
Types of Master Cylinder
Single Circuit Master Cylinder
Tandem Master Cylinder or Dual Circuit Master Cylinder

## Slide 22: Components of Hydraulic Brakes
Single Circuit Master Cylinder
It is the simple type of master cylinder just like a medical syringe, in this type of master cylinder single piston inside a cylinder is used to cause braking.
Single circuit master cylinder distributes equal force in all the wheels due to the use of single cylinder single piston or circuit.
This type of master cylinder is commonly used in many 3 wheelers and some light weight 4 wheelers

## Slide 23: Components of Hydraulic Brakes
It consist of 5 parts :-
1. Reservoir
It is the storage tank used for storing the brake fluid in hydraulic type of braking system, usually it is made up of plastic.
2. Cylinder
It is the air tight housing inside which the piston moves with the movement of brake pedal which in turn causes conversion and multiplication of force. Cylinder is usually made up of cast iron or aluminum.
It is connected with the reservoir through inlet valve and also with brake lines through outlet valve.
In single circuit master cylinder, there is only 1 compression chamber.

## Slide 24: Components of Hydraulic Brakes
3. Piston
It is the reciprocating part of the master cylinder that reciprocates inside the cylinder due to the movement of brake pedal, the piston causes compression of brake fluid inside the cylinder which in turn generates high hydraulic pressure.
In single circuit only 1 piston is used.
4. Returning Spring
It is the simple coil type of spring used inside the cylinder which helps the piston and brake pedal to retain its original position after brake pedal is released.

## Slide 25: Components of Hydraulic Brakes
5. Valve
In single circuit master cylinder, it is the outlet valve through which the brake line is attached
The compressed brake fluid is further transferred to the wheel cylinder through this valve

## Slide 27: Components of Hydraulic Brakes
Tandem Master Cylinder or Dual Circuit Master Cylinder
It is the modified type of single circuit master cylinder in which dual cylinder-dual piston or single cylinder dual piston along with dual circuit is used for independent braking between front and rear wheels.
This type of master cylinder is used in almost all cars as it is more efficient than single circuit master cylinder.
It provides the independency between front and rear wheels braking or diagonal type of braking which is the important safety feature for a vehicle

## Slide 28: Components of Hydraulic Brakes
It consists of:-
1.Reservoir
In tandem master cylinder instead of single reservoir 2 or dual chamber reservoir is used as a storage tank for brake fluid.
2. Cylinder
Same cylinder as in single circuit type is used with the little modification i.e. it is the housing of 2 pistons and also there are 2 outlet and 2 inlet valves.
In tandem m c there are 2 compression chamber inside the cylinder.

## Slide 29: Components of Hydraulic Brakes
3. Piston
Instead of one piston, 2 pistons that are primary piston and secondary piston are used in tandem M C, the actuation of secondary piston occurs after completion of the primary piston movement.
Primary piston is connected to the brake pedal and secondary piston is placed just behind the returning spring of primary piston.
4. Returning Spring
In tandem MC 2 returning springs are used one with the primary piston and second with the secondary piston.
5. Valves
In tandem master cylinder as it is the dual circuit MC , 2 inlet and 2 outlet valves are used .

## Slide 31: Components of Hydraulic Brakes
Brake Pipe and Hoses
Brake pipe is a rigid (usually steel) pipe that transfers pressurized brake fluid from the master cylinder, where brake fluid is stored, to the brake hoses.
Brake hoses are the flexible hoses that connected to the caliper or wheel cylinder.
They must be flexible in order to accommodate for the vehicle's suspension travel when turning the wheels and traveling over uneven surfaces

## Slide 34: Components of Hydraulic Brakes
Regulating valves
This involves
• The metering valve
• The pressure differential switch and
• The proportioning valve

## Slide 35: Components of Hydraulic Brakes
Metering Valve
The metering valve section of the combination valve is required on cars that have disc brakes on the front wheels and drum brakes on the rear wheels.
This configuration requires that the disc brake pad is normally in contact with the disc, while the drum brake shoes are normally pulled away from the drum. Because of this, the disc brakes are in a position to engage before the drum brakes when you push the brake pedal down.

## Slide 36: Components of Hydraulic Brakes
Metering Valve cont..
The metering valve compensates for this, making the drum brakes engage just before the disc brakes.
The metering valve does not allow any pressure to the disc brakes until a threshold pressure has been reached.
The threshold pressure is low compared to the maximum pressure in the braking system, so the drum brakes just barely engage before the disc brakes kick in.
Having the rear brakes engage before the front brakes provides a lot more stability during braking.
Applying the rear brakes first helps keep the car in a straight line

## Slide 37: Components of Hydraulic Brakes
Pressure Differential Switch
The pressure differential valve is the device that alerts you if you have a leak in one of your brake circuits.
The valve contains a specially shaped piston in the middle of a cylinder.
Each side of the piston is exposed to the pressure in one of the two brake circuits.
As long as the pressure in both circuits is the same, the piston will stay centered in its cylinder.
But if one side develops a leak, the pressure will drop in that circuit, forcing the piston off-center.
This closes a switch, which turns on a light in the instrument panel of the car

## Slide 38: Components of Hydraulic Brakes
Proportioning Valve
The proportioning valve reduces the pressure to the rear brakes.
Regardless of what type of brakes a car has, the rear brakes require less force than the front brakes.
The amount of brake force that can be applied to a wheel without locking it depends on the amount of weight on the wheel.
More weight means more brake force can be applied.
If you have ever slammed on your brakes, you know that an abrupt stop makes your car lean forward..

## Slide 39: Components of Hydraulic Brakes
Proportioning Valve cont..
The front gets lower and the back gets higher.
This is because a lot of weight is transferred to the front of the car when you stop. Also, most cars have more weight over the front wheels to start with because that is where the engine is located
If equal braking force were applied at all four wheels during a stop, the rear wheels would lock up before the front wheels.
The proportioning valve only lets a certain portion of the pressure through to the rear wheels so that the front wheels apply more braking force

## Slide 41: Components of Hydraulic Brakes
Foundation brakes
Foundation, or wheel brakes, divide into two distinct classes, namely
Disc and
Drum(radial) brakes.
The foundation brake consists of
Brake drum/rotor
Backing plate
Brake shoes/Caliper with pads
Wheel cylinder

## Slide 42: Components of Hydraulic Brakes
A. Disc Brake
The main components of a disc brake are
Brake pads
Caliper, which contains a piston and
Rotor, which is mounted to the hub.

## Slide 44: Components of Hydraulic Brakes
A. Disc Brake Cont..
The disc brake is a lot like the brakes on a bicycle.
Bicycle brakes have a caliper, which squeezes the brake pads against the wheel. In a disc brake, the brake pads squeeze the rotor instead of the wheel, and the force is transmitted hydraulically instead of through a cable.
Friction between the pads and the disc slows the disc down

## Slide 45: Components of Hydraulic Brakes
A. Disc Brake Cont..
The disc/rotor on disc brake can be
Solid or
Vented
Vented disc brakes have a set of vanes, between the two sides of the disc that pumps air through the disc to provide cooling.

## Slide 47: Components of Hydraulic Brakes
A. Disc Brake Cont..
Brake caliper can be
a. Floating caliper
b. Fixed caliper

## Slide 48: Components of Hydraulic Brakes
a. Floating caliper
The single-piston floating-caliper disc brake is self-centering and self-adjusting.
The caliper is able to slide from side to side so it will move to the center each time the brakes are applied.
Also, since there is no spring to pull the pads away from the disc, the pads always stay in light contact with the rotor.
This is important because the pistons in the brakes are much larger in diameter than the ones in the master cylinder.
If the brake pistons retracted into their cylinders, it might take several applications of the brake pedal to pump enough fluid into the brake cylinder to engage the brake pads.

## Slide 50: Components of Hydraulic Brakes
b. Fixed caliper
This type has dual or four-pistons.
A piston (or two) on each side of the rotor pushed the pad on that side.
This design has been largely eliminated because single-piston designs are cheaper and more reliable.

## Slide 52: Components of Hydraulic Brakes
Hand/Emergency Brakes in Disc Brake
In cars with disc brakes, an emergency/hand brake has to be actuated by a separate mechanism than the primary brakes in case of a total primary brake failure.
Most cars use a cable to actuate the emergency hand brake.

## Slide 53: Servicing Disc Brakes
The most common type of service required for brakes is changing the pads. Brake pads usually have a piece of metal on them called a wear indicator
When enough of the friction material is worn away, the wear indicator will contact the disc and make a squealing sound.
This means it is time for new brake pads.

## Slide 55: Servicing Disc Brakes
There is also an inspection opening in the caliper so you can see how much friction material is left on your brake pads. Sometimes, deep scores get worn into brake rotors.
This can happen if a worn-out brake pad is left on the car for too long.
Brake rotors can also warp; that is, lose their flatness.
If this happens, the brakes may shudder or vibrate when you stop.
Both of these problems can sometimes be fixed by refinishing (also called turning or machining) the rotors.
Some material is removed from both sides of the rotors to restore the flat, smooth surface.

## Slide 56: Servicing Disc Brakes
Refinishing is not required every time your brake pads are replaced.
You need it only if they are warped or badly scored.
In fact, refinishing the rotors more often than is necessary will reduce their life. Because the process removes material, brake rotors get thinner every time they are refinished.
All brake rotors have a specification for the minimum allowable thickness before they need to be replaced.
This specification can be found in the manufacturer’s manual for each vehicle.

## Slide 57: Components of Hydraulic Brakes
B. Drum Brakes
Drum brakes are a brake system with brake drums which rotate with the wheels.
Inside each drum are brake shoes fitted with brake linings (friction material). Pistons (pressure mechanism) press against the drums from the inside to generate braking force, thus making is possible to decelerate and stop the vehicle.

## Slide 59: Components of Hydraulic Brakes
There are three types of drum brakes depending on how the brake shoes are pressed on to the drums
Leading and trailing shoes
Twin leading shoes
Duo-servo

## Slide 60: Components of Hydraulic Brakes
a. Leading and trailing shoes
Leading (or primary) shoe" is a term referring to the shoe that moves in the direction of rotation when it is being pressed against the drum.
The other shoe is called the “trailing (secondary) shoe.”
The leading shoe is pressed in the same direction as the rotation of the drums, and this rotation helps to press the shoes against the drum with greater pressure for stronger braking force.
This is called the servo effect (self-boosting effect) which realizes the powerful braking forces of drum brakes.

## Slide 61: Components of Hydraulic Brakes
a. Leading and trailing shoes Cont..
Structurally, it has a wheel cylinder(double acting) housing a piston with which hydraulic pressure is generated to push the two shoes against the drum’s inner surface.
The two shoes function in a way they both become either the trailing shoe or leading shoe depending on whether the vehicle is travelling forward or backward.
Drum brakes generate consistent braking force whether the vehicle travels forward or backward.
This is because drum brakes generate the same braking force in either direction.
Generally, this type is used for the rear brakes of passenger cars.

## Slide 64: Components of Hydraulic Brakes
b. Twin/two leading shoes
This type of drum brake has two-wheel cylinders and two leading shoes.
Each wheel cylinder presses on one shoe, so that both shoes act as leading ones when the vehicle moves forward, providing superior braking force.
Each of the pistons housed in the wheel cylinders displace in one direction, so when the vehicle is in reverse both shoes act as trailing ones.
This type is used mainly for the front brakes of small-to-mid-sized trucks

## Slide 66: Components of Hydraulic Brakes
c. Duo Servo
Duo-servo drum brake systems have a pair of brake shoes called the primary shoe and secondary shoe linked by a hydraulic wheel cylinder near the top and linked by an adjuster at the bottom.
Strong pressure from the servo effect (self-boosting effect) of the primary shoe is transmitted to the linked secondary shoe, thus generated a very large braking force.
The uppermost ends of the shoes rest against an anchor pin above the wheel cylinder.

## Slide 68: Components of Hydraulic Brakes
The Emergency Hand Brake in Drum Brake
The emergency hand brake on a car has to be actuated by a different power source than the primary braking system.
The drum brake design allows for a simple cable actuation mechanism.
When the emergency brake is actuated, a cable pulls on the lever, which forces the two shoes apart
NOTE
Other vehicle the parking brake mechanism is placed in propeller shaft due to length of the vehicle

## Slide 70: Servicing Drum Brake
The most common service required for drum brakes is adjusting and changing the brake shoes.
Some drum brakes provide an inspection hole on the back side, where you can see how much material is left on the shoe.
Brake shoes should be replaced when the friction material has worn
If the friction material is bonded (no rivets), then the shoes should be replaced when they have only 1.6 mm of material left.

## Slide 71: Servicing Drum Brake
Just as in disc brakes, deep scores sometimes get worn into brake drums.
If a worn-out brake shoe is used for too long, the rivets that hold the friction material to the backing can wear grooves into the drum.
A badly scored drum can sometimes be repaired by refinishing.
Where disc brakes have a minimum allowable thickness, drum brakes have a maximum allowable diameter.
Since the contact surface is the inside of the drum, as you remove material from the drum brake the diameter gets bigger

## Slide 73: Servicing Drum Brake
Bake bleeding
Bake bleeding is the procedure performed on hydraulic brake system where by the brake lines are purged of any air bubbles
This is necessary because while the brake fluid is an incompressible liquid, air bubbles are compressible gas and their presence in the brake system greatly reduces the hydraulic pressure that can be developed within the system
The process is performed by forcing clean, bubbles free brake fluid through the entire system usually from master cylinder to wheel cylinders

## Slide 74: Servicing Drum Brake
Bake bleeding Cont..
A brake bleed screw is normally mounted at the highest point on each cylinder or caliper
There are various methods of brake bleeding as follows
The pump and hold method
By using vacuum pump method
By using pressure pump
Gravity

## Slide 75: Anti-locking brake system
Anti-lock braking system (ABS) is an automobile safety system that allows the wheels on a motor vehicle to maintain tractive contact with the road surface according to driver inputs while braking, preventing the wheels from locking up (ceasing rotation) and avoiding uncontrolled skidding.
It does this at a much faster rate and with better control than a driver could manage

## Slide 76: Anti-locking brake system
Purposes of ABS
Offers improved vehicle control
Decreases stopping distances on dry and slippery surfaces
On loose surfaces like gravel or snow-covered pavement, ABS can significantly increase braking distance, although still improving vehicle control

## Slide 77: Anti-locking brake system
Components of ABS
Wheel speed sensor
Used to determine the acceleration or deceleration of the wheel.
Controller/ECU
Control the system (receives signal from sensors and actuates pump/valves)
Pump
Used to restore the pressure to the hydraulic brakes after the valves have released it
ABS malfunction indicator lamps
Indicates if there is fault or problem in ABS system

## Slide 78
Wheel speed sensor (A), ABS control module (B), hydraulic motor and pressure release valves (C), Brake pipe leading to caliper (D)

## Slide 79: Anti-locking brake system(ABS)
Operation Of ABS
Typically, ABS includes a central electronic control unit (ECU), four-wheel speed sensors, and hydraulic valves within the brake hydraulics.
The ECU constantly monitors the rotational speed of each wheel.
If it detects a wheel rotating significantly slower than the others, a condition indicative of impending wheel lock, it actuates the valves to reduce hydraulic pressure to the brake at the affected wheel, thus reducing the braking force on that wheel, the wheel then turns faster

## Slide 80: Anti-locking brake system
Operation Of ABS Cont..
Conversely, if the ECU detects a wheel turning significantly faster than the others, brake hydraulic pressure to the wheel is increased so the braking force is reapplied, slowing down the wheel.
This process is repeated continuously and can be detected by the driver via brake pedal pulsation.
Some anti-lock systems can apply or release braking pressure 15 times per second.
Because of this, the wheels of cars equipped with ABS are practically impossible to lock even during panic braking in extreme conditions

## Slide 82: Anti-locking brake system
Types of ABS Channels
There are two main types of modern ABS systems:
1.Three channel
2. Four channel.

## Slide 83: Anti-locking brake system
Three channel systems
Control the braking pressure on both front wheels independently, but control the rear wheels together as a single unit.

## Slide 85: Anti-locking brake system
Four channel systems
Control the brake force on each wheel independently (assuming you're in a four wheeled vehicle)