## Slide 1: PRESSURE MEASUREMENT
INTRODUCTION TO PRESSURE

## Slide 2: Learning objectives
At the end of this discussion the participants should be able to;
Explain the meaning of the term pressure
Describe factors affecting pressure in both liquid and gas
Describe pressure measurement principles

## Slide 4: INTRODUCTION
The measurement of pressure is one of the major process of measurement used for process control. The pressure of almost any liquid or gas that is stored or moved must be known to ensure safe and reliable operation.
Pressure is defined as a force divided by the area over which the force is applied. However force is pull or push that changes or tend to change the state of rest or motion of a body.
Also area is the number of unit squares equal to the surface of an object.

## Slide 5: Introduction ………

## Slide 6: PRESSURE MEASUREMENT
Pressure is the amount of force applied over a defined area. The relationship between pressure, force and area is represented by the following formula.
P = F/A
Where: P = Pressure
F = Force
A = Area
The SI units for pressure N/m2,Pa, bar, psi

## Slide 7: Introduction to pressure cont…..
If a force (due to physical contact) is applied over an area, pressure is being created. Pressure increases if force increases or the size of the area over which the force being applied decreases.

## Slide 8: PRESSURE VARIABLES
Factors that influence the pressure of liquid are different from factors that influence the pressure of gas.
Therefore when measuring pressure it is important to understand the pressure properties of liquid or gases.
Hydrostatic pressure (head pressure)
The pressure exerted by a liquid is influenced by three factors namely; (a) Height of liquid in a column (b) density of the liquid ( c) Vapour in the liquid

## Slide 9: Liquid level
The pressure at the bottom of a column of liquid increases as the height of the liquid in the column increase.
Pressure is affected by the height rather than the volume of a liquid.
If other factors remain constant e.g. Density and pressure on surface of the liquid, the pressure at a bottom of larger diameter tank will be equal to that of a smaller diameter tank when the height of the liquid is the same.

## Slide 10: How height of liquid affect pressure

## Slide 11: Hydrostatic pressure
Hydrostatic pressure is the pressure which rises above a certain level in a liquid owing to the weight of a liquid mass.
Ps = ρgh where;
Ps =hydrostatic pressure (gravitational pressure) in Pascal
ρ = density of liquid in kg/m3
h = level of column in m
g = acceleration due to gravity in m/s2

## Slide 12: Hydrostatic pressure cont….
In accordance with the SI International system of units, hydrostatic pressure is given in both Pascal and bar.
The level of the column of liquid is given the unit ‘’metre’’, the density of the liquid ‘’kilogram per cubic metre’’and the acceleration due to gravity ‘’metre per second square’’.

## Slide 13: Density of a liquid
Density is the mass of a particular substance per unit volume.
Density = mass/volume
Liquid with a greater density has a greater mass per unit of volume.
Liquid with greater densities will produce greater hydrostatic pressure (head) than liquids with lower densities.

## Slide 14: Pressure on gas
Unlike liquid, a gas will exert pressure on all parts of the container in which it occupies.
Factors affecting pressure on gas
Two factors affect the pressure exerted by gas;
Volume of the container in which gas is held
The temperature of the gas

## Slide 15: Gas pressure Vs Volume relationship
At constant temperature, the relationship between pressure (P) exerted by a gas and the volume of the container (V) in which the gas is held is known as Boyle’s law.
Because a gas can be compressed, the pressure of a gas increases proportionally as the volume of the container in which the gas is held decreases.
PV = constant
Boyle’s law: P1V1 = P2V2

## Slide 16: Gas pressure Vs Volume cont..
Conversely, if a certain amount of gas is transferred to a larger container the pressure will decrease in proportion to the increase in container’s volume.
From P1V1 = P2V2; but V1 =40m3 and V2 =2V1
i.e. 2X40 =80m3
thus; P1X40 = P2x80;
P2 = (P1 x40)/80
Then, P2 = 1/2P1
Therefore pressure will decrease by half

## Slide 17: Gas Pressure Vs Volume and Temperature
Gas pressure is affected by changes in temperature. As the temperature of the gas increases, the energy of the individual molecules increases as well.
This in turn causes the molecules to collide with the vessel’s wall more frequently and with greater force and the pressure exerted against the inside wall of the vessel increases.

## Slide 18: Gas Pressure Vs Volume and Temperature cont…
If the volume of the vessel holding the gas and the amount of gas remain unchanged, the pressure exerted by the gas on the vessel wall will change in proportion to change in the temperature of the gas.

## Slide 19: PRESSURE MEASUREMENT
Pressure measurement devices can be categorized according to the measured reference pressure.
Reference pressure is the pressure measurement that is compared to the actual measured pressure of the process.
There are three reference pressure namely;
    Absolute pressure
    Gauge pressure and
    Differential pressure

## Slide 20: Pressure reference cont……..
Absolute and Gauge pressure: These measures the difference between the pressure of the process fluid and reference pressure.
Differential pressure takes two pressure measurements of the process fluid at different point and compute the difference.

## Slide 21: Absolute pressure
This measures pressure to a perfect volume (zero pound per square inch). Because no pressure reading can be less than a perfect volume, an absolute pressure measurement device will never have a negative reading.

## Slide 22: Gauge pressure
A gauge pressure transmitter has its low side referenced to the surrounding atmosphere, approximately 14.7psi or 101.6kPa, the high side then measure the process.
Changes in atmospheric pressure will impact the process in the low side and there will be no impact to the high side.
Gauge pressure transmitters are often used to measure pressure in pipes or liquid level in an open tank.

## Slide 23: Differential pressure
A differential pressure transmitter has both its high and low side connected to the process.
Changes in the atmospheric pressure does not affect the output of differential pressure measurement instrumentation because both measured pressure and referenced pressure are equally influenced by exposure to the atmosphere.
Differential pressure transmitters are often used to measure flow or liquid level in a closed tank.

## Slide 24: Measured pressure
The three pressure in the process control industry include;
  Head pressure
  Static pressure and
  Vapor pressure
(1). Head pressure.
This is also known as hydrostatic pressure, it is the pressure exerted by a column of a fluid. It is directly proportional to the specific gravity (sg) of the fluid and the height of the fluid column.

## Slide 25: Head pressure

## Slide 26: Static pressure
Static pressure or line pressure is the pressure exerted in a closed system. It is mostly common measured in flow application and refers to the pressure exerted by the fluid in the pipe.
Another example of static pressure can be found in boiler system; as the water in the boiler is heated, pressure increases.

## Slide 27: Vapor pressure
Vapor pressure is the result of fluid vaporization and is a measured pressure in the closed system.
Vaporization is the transformation of a substance from a liquid state to a gaseous state. eg water to steam
The transformation occurs at a specific temperature for each liquid. eg. Water turns to liquid (boils) at 212°F or 100°C.
Vapor pressure is mostly common measured in closed tank direct pressure application whereby vapor pressure is low side transmitter measurement.

## Slide 28: Pressure application
Type | Definition | Application Examples
Gauge | Reference to atmospheric pressure. | Car Tyre Water Level Measurement Chamber Pressure Hydraulic Applications
Sealed | Referenced to a sealed chamber closed with atmospheric pressure (approximately 1bar). | For use in Aggressive Media Industrial Applications Washdown Environments Food and Beverage
Absolute | The reference is a vacuum (0bar or no pressure). | Barometric Weather Stations and Meteorological Applications

## Slide 29: Pressure application…
Differential | Measuring the difference between two pressure port readings. | -Filter and Pump Monitoring -Air Conditioner HVAC Heating -Ventilation and Air Conditioning - Clean Room Monitoring