## Slide 1: SYSTEM CONTROLLERS
INTRODUCTION

## Slide 2: Learning objective.
At the end of this lecture participants should be able to;
    Define the term controller
    Describes electrical, electronic, pneumatic and hydraulic controllers
    Identify pneumatic system components
    Identify hydraulic system components
    Describe importance of controllers

## Slide 3: The concept of controllers
Introduction
A controller is a comparative device that receives an input signal from a measured process variable, compare this value with that of predetermined control point value (set point) and determine the appropriate amount of output signal required by the final control element by providing corrective action within a control loop.

## Slide 4: Introduction cont….
A controller is a mechanism that seeks to minimize the difference between the actual value of a system (i.e. the process variable) and the desired value of the system (i.e. the set-point).
Controllers are a fundamental part of control engineering and used in all complex control systems

## Slide 5: Why system controllers?
Controllers improve the steady-state accuracy by decreasing the steady state error.
As the steady-state accuracy improves, the stability also improves.
Controllers also help in reducing the unwanted offsets produced by the system.
Controllers can control the maximum overshoot of the system.

## Slide 6: Why system controller cont…
Controllers can help in reducing the noise signals produced by the system.
Controllers can help to speed up the slow response of an over-damped system.

## Slide 7: Types of controllers
System controllers may be divided into several categories depending on energy used, construction and parameters they control etc
Basing on energy used; we have:
  Electrical controllers
  Pneumatic controllers
  Hydraulic controller

## Slide 8: 1. Electrical controllers
Electrical control device provide ON/OFF or two-position control. In residential and small commercial application low voltage electrical controls are most common.
A transformer is used to reduce 220volts alternating current (AC) to a normal 24 volts. This voltage signal is controlled by a thermostat and can open solenoid valves, energize oil burner, control electric heat, operate two position valves and dampers or turn ON/OFF fans and pumps.

## Slide 9: Electric controller cont………
A relay or contactor is used to switch the line voltage equipment with the low voltage control signal. Also the refrigerator guard is put in wall socket to protect the appliance form electric shocks.
The advantage of electric controller system is that it enhance the personal safety and eliminate fire risk associated within the line voltage.

## Slide 10: Electronic controllers
An electronic sensor (thermocouple, Resistance Temperature Detector- RTD) installed at the measurement location continuously sends an input signal to the controllers.
At set intervals the controllers compares this signal deviates to a predetermined set point.
If the input signal deviates from the set point, the controller sends a corrective output signal to the control element. This electric signal must be converted to the appropriate signal for easy interpretation.

## Slide 11: Features of electronic controllers
An electronic controller is best suited for application where large load changes are encountered and or fast response changes are required.

## Slide 12: Characteristics of electronic controllers
The input: This is the measurement signal received by the controller from the sensor. A variety of input types are available including thermocouple, RTD, voltage, current etc.
The control output: This is the corrective signal transmitted from the controller to the control element. Various control output types are available including contact, voltage, current etc.

## Slide 13: Characteristics cont…..
Alarms: Most models can be ordered with alarms event outputs or heater break alarms, which signal an external device to perform a specific task at a predetermined set point.
Setback function: This feature, optionally available on some models is designed to provide energy savings in application where the process is idle at regular intervals through the connection of an external time or switch.

## Slide 14: 2. Pneumatic controllers
Introduction to pneumatics.
A pneumatic is a system that uses compressed air to transport a control energy. Air is first pressurerized to give energy in the cylinder. The signals are input in the system through the use of switches and the air is transferred through sealed pipes to the pneumatic parts for processing.

## Slide 15: Introduction cont…..
Finally the force produced by the pneumatic parts is utilized to finish the designated task.
The use of pneumatic system is very extensive for example in controlling the movement of train doors, automation of production lines etc.

## Slide 16: Components of pneumatic system
Compressor
The compressed air supply for a pneumatic system should be adequately calculated and made available in the appropriate quality.
Air is compressed in an air compressor and delivered to an air distribution system.

## Slide 17: Components of pneumatic cont….
2. Valves
The function of a valve is to control the pressure or flow rate of pressure media. Depending on design valves are divided into the following categories
Directional valves
    Input or signaling element
    Processing element
    Control element

## Slide 18: Categories of valves cont…
ii. Non return valve
iii. Flow control valve
iv. Pressure control valve
    Pressure limiting valve
    Pressure regulator valve
    Pressure sequence valve
v. Shut-off valve

## Slide 19: 3. Processing element (processor)
This is used to support the directional valve at the processing level, there are various elements which condition the control signals for a task. The elements are:
    Dual pressure valve (AND function)
    Shut-off valve (OR function)

## Slide 20: 4. The power section
The power section consists of control elements and power components or actuators to transmit the power generated
The characteristics are further divided into;
1. Linear actuators
  Single acting cylinder
  double acting cylinder
  2. Rotary actuators
  Air motor
  Rotary actuator

## Slide 21: 5. Systems
Generally the actuation of cylinder is effected via directional control valve. The choice of such a directional control valve depends on the respective applications such as;
    Number of connections
    Number of switching position
    Type of actuation

## Slide 22: Pneumatic system overview
The system can be very simple, for example a switch is only needed in controlling a light bulb to work.
However the advancement of technology geared most of the control systems gradually became complicated and that various parts are involved.

## Slide 23: System overview cont…….
Consider a lift as an example, it needs a number of parts to be cooperative in operation so as to transport passengers to different station safely and at a set time.
A system may comprise of some relative small parts known as sub systems. These includes driving system, door opening system, control system, safety system, lighting system, ventilation system and security system.

## Slide 24: Lift system illustration
The chart below illustrate lift system
Lift system
Driving system
Door opening system
Control system
Safety system
Lighting system
Security system
Ventilation system

## Slide 25: Lift system illustration cont…..
In fact each system can be considered as an independent system that includes input, process and out put. While there exist relationship between the sub-system that an output of one sub system may become the input of another system. The output generated from control system may affect the driving and door opening systems.

## Slide 26: illustration cont…….
Therefore when analyzing a complicated control system, that system can be divided into several comparatively simple sub systems so as to familiarize with the operation of the whole system easily. Besides, based on the sub- system concept, we would understand the relationship of parts of the whole system much easier.

## Slide 27: Hydraulic system controllers
Hydraulic systems are used to transfer power energy. Hydraulic means generation of force and motion for the purpose of power transmission. However not all fluids are suitable to transfer power energy, for instance water can not be used in hydraulic systems as a means of power energy transfer due to the following weakness;
  weak to corrosion resistance
  low boiling point
  low freezing point
  low viscosity

## Slide 28: Components of hydraulic system
The following are the components of hydraulics systems.
Power supply section
The power supply unit provides the necessary hydraulics power by converting the mechanical power from the drive motor.
The most important component in the power supply unit is the hydraulic pump.

## Slide 29: Power supply section cont…….
This draws in the hydraulic fluid from a reservoir (tank) and delivers it via a system of lines in the hydraulic installation against the opposing resistances.
Pressure does not build up until the flowing liquid encounter a resistance.

## Slide 30: (ii). Hydraulic fluid
This is the working medium which transfers the prepared energy from the power supply unit to the drive section (cylinders or motors)
Hydraulic fluids have a wide variety of characteristics. Therefore they must be selected to suit the application. Hydraulics on a mineral oil base are frequently used, these are referred to as hydraulic oils.

## Slide 31: (iii) Valves
These are devices for controlling the energy flow. They can control and regulate the flow direction of the hydraulic fluid, the pressure, the flow rate and consequently the flow velocity.

## Slide 32: Qualities of hydraulic fluids
Lowest possible density
Minimal compressibility
Lubricating film viscosity
Good viscosity-pressure characteristics
Good viscosity- temperature characteristics
Low flammability
Resistant to cold
Wear and corrosion protection
Water separable
Air release

## Slide 33: Functions of hydraulic fluids
The hydraulic fluid in hydraulic systems are used to perform the following functions
Transfer of power
Lubrication of moving parts of devices
Cooling i.e. diversion of heat produced by energy conversion
Cushioning of oscillations caused by power jerks
Corrosion resistance
Removal of scuff ( debris material)
Signal transmission

## Slide 34: Application of hydraulics
A: Stationary hydraulics
Production and assembly machines
Transfer lines
Lifting conveying devices
Press machines
Rolling machines
Lifts etc.

## Slide 35: Application of hydraulics cont…..
B: Mobile hydraulics
Construction machines
Tippers, excavators, elevating platform
Lifting and conveying devices
Agricultural machinery

## Slide 36: Importance of controllers
Providing feedback for system control and correctness of variables
Enhance safety of production systems
Promote higher production as it save time and minimize rejects
Enhance smooth operation of machine and equipment